## Slide 1: 3 CFU Stage: ThingsBoard & PYNQ
Daniel Amadori

## Slide 2: Presentation
Add slides to the Prof. Fummi’s presentation:
  Describe possible sources of IoMT data
  Analysis of the differences/similarities between IoT and IoMT
  Overview of ThingsBoard example
ThingsBoard example presentation:
  Detailed tutorial of MQTT + PYNQ + Sensors  ThingsBoard
  PYNQ-Z1 board
  Use the GPIOs of the PYNQ board to interface with sensors (IoT & IoMT)
    Collect data and publish it to ThingsBoard through MQTT
    pip3 install tb-mqtt-client
  ThingsBoard Dashboards

## Slide 3: ThingsBoard example
Work From Home phase:
  Environment setup + collect telemetry data
    cpu_usage, ip_address, mac_ address, processes_count, swap_memory_usage, ram_usage, avg_load, boot_time, battery level, etc…
    Dashboards for telemetry visualization
  Various sensors integration (IoT & IoMT)
    Dashboards for IoT & IoMT
IN-Presence phase (to be planned in :
  PYNQ environment setup
  Test-on board + hw sensors integration
  Control PYNQ led + PYNQ buttons on-press

## Slide 4: ThingsBoard
MQTT Client
Sensors
MQTT
Broker
ThingsBoard
Gateway

## Slide 5: ThingsBoard
Download at link, install and Log in to ThingsBoard:
  Open your web browser and navigate to the ThingsBoard instance (e.g., http://localhost:8080)
  Log in with Tenant Administrator credentials
  Type of Users:
    System Administrator: (user: sysadmin@thingsboard.org, psswd: sysadmin)
      Create Tenant & Tenant Administrator
      Configure: Mail server, SMS provider, 2FA, OAuth 2, Slack
    Tenant Administrator: (user: tenant@thingsboard.org, psswd: tenant)
      Create device, dashboard, alarm, customer and assign dashboard
      Connect device
      Configure alarm rules
    Customer User: (user: customer@thingsboard.org, psswd: customer)
      Read-Only Access
      Monitor devices, assets, entity (real-time/historical data)
      Alarm Viewing

## Slide 6: How to Create a Device
Create a new Device (link):
  Navigate to the 'Devices' section
  Click the '+' button and enter a name and optional description.
  Click ‘Add new Device' to create the device.
  Enter a name for your device (e.g., "Dev0")
  Enter a device profile (e.g., PYNQ-Z1)
  Click "Add" to create the device.
Check connectivity (link):
  Use the command provided by the platform

## Slide 7: How to Create an Asset
Create a new Asset:
  Navigate to the 'Asset' section
  Click the '+' button and enter a name
  Click ‘Add’
Assign device to Asset (link):
  Click to the selected asset
  Select ‘RELATIONS’ in the tab menu
  Click the '+' buttons
  Select:
    ‘Contains’ as relation type
    ‘Device’ as entity
  Add the device to the entity list

## Slide 8: How to Create a Dashboard in ThingsBoard
Create Dashboards (link):
  Navigate to the "Dashboards" page through the main menu on the left
  Click the "+" sign in the upper right corner of the screen
  Select "Create new dashboard" from the drop-down menu
  In the opened dialog write the dashboard:
    Title (e.g. Telemetry, Healthcare, Ambiental)
    Description is optional
  Click "Add"

## Slide 9: How to Create a Dashboard in ThingsBoard
Create Aliases:
  Click "Aliases" in the upper right corner of the screen
  Click “Add Alias“
  In the opened dialog write the Name (e.g. All devices) and select:
    ‘Solve as multiple Entity’
    ‘Query search device’ as ‘Type of filter’
    ‘Asset’ as ‘Type’
    your asset as ‘Asset’
    ‘Contains’ as ‘Type of relation’
    Your type of device as ‘Type of device’
  Click “Add“

## Slide 10: How to Create a Dashboard in ThingsBoard
Create Aliases:
  Click “Add Alias“
  In the opened dialog:
    Write the Name (e.g. Current device)
    Select ‘Entity from dashboard state’ as ‘Type of filter’
  Click “Add“
  Click “Save“

## Slide 11: How to Create a Dashboard in ThingsBoard
Create States:
  Click “States“ in the upper left corner of the screen
  Click the "+" sign in the upper right corner of the opened dialog
  In the new opened dialog write:
    Name (e.g. ${entityName}: Telemetry details)
    Id state (e.g. telemetry_details)
  Click “Add“
  Click “Save“

## Slide 12: How to Create a Dashboard in ThingsBoard
Create Dashboards Entity Widget:
  Select the default state
  Click the "Add widget" button at the top
  Select ‘Entities table’ in the ‘Tables’ section
  Select ‘Advanced’ in the upper right corner of the opened dialog
  Create Datasource, select:
    Select ‘Entity’ as ‘Type’
    Select the alias you create (e.g. All devices) as ‘Alias entity’
    Add all the time series (e.g. cpu_usage, heart_rate)

## Slide 13: How to Create a Dashboard in ThingsBoard
Create Dashboards Entity Widget:
  Create Action:
    Click “Action“
    Click the "+“
    In the new opened dialog:
      Write the name: (e.g. to_details)
      Select ‘on row click’ as ‘Source Action’
      Select the desired state (e.g. telemetry_details)
  Click “Add“
  Click “Add“
  Resize the table as you want
  Save

## Slide 14: How to Create a Dashboard in ThingsBoard
Create Dashboards Device Widget (link):
  Select the created state (e.g. telemetry_details)
  Click the "Add widget" button at the top
  Find and select the desired widget
  Select ‘Advanced’ in the upper right corner of the opened dialog
  Create Datasource, select:
    Select ‘Entity’ as ‘Type’
    Select the alias you create (e.g. Current device) as ‘Alias entity’
    Add all the time series (e.g. cpu_usage, heart_rate)

## Slide 15: How to Create a Dashboard in ThingsBoard
Create Dashboards Device Widget (link):
  Modify Widget:
    Select ‘Widget card’ in the top of the opened dialog
    Write the title (e.g. ${entityName}: Time series chart)
  Click “Add“
  Resize the table as you want
  Save

## Slide 16: How to Create a Dashboard in ThingsBoard
Create Dashboards Device Alarm Widget:
  Select the created state (e.g. telemetry_details)
  Click the "Add widget" button at the top
  Find and select the desired alarm widget (Alarm table, Alarm count)
  Select ‘Basic’ in the upper right corner of the opened dialog
  Create Alarm source, select:
    Select ‘Alias entity’ instead of ‘Device’
    Select the alias you create (e.g. Current device) as ‘Alias entity’
    Select the ‘Alarm type list’ (e.g. critical_temperature)

## Slide 17: How to Create a Dashboard in ThingsBoard
Create Dashboards Device Alarm Widget:
  Modify Widget:
    Write the card title (e.g. ${entityName}: Alarms)
  Click “Add“
  Resize the widget as you want
  Save

## Slide 18: Example of Dashboard in ThingsBoard

## Slide 19: Example of Dashboard in ThingsBoard

## Slide 20: Example of Dashboard in ThingsBoard

## Slide 21: Example of Dashboard in ThingsBoard

## Slide 22: How to Create an Alarm rules in ThingsBoard
Create a Rule chain:
  Click the ‘Rule chain’ in the sidebar
  Click the ‘+’ and after select ‘Add new Rule Chain’
  In the new opened dialog:
    Write the name: (e.g. Telemetry Rules)
  Create a diagram (image)
    Script:
      write name (e.g. Battery Threshold)
      Javascript code with the feature and the threshold (e.g. ‘return msg.battery_level < 5’;)
    Arrow: select condition (e.g. True, False, Success, None)
    create alarm:
      write name (e.g. Battery Alarm)
      Alarm type (e.g. Critical Battery Level)
      Alarm severity (e.g. Critical, Advise, ..)
  Save

## Slide 23: How to Create an Alarm rules in ThingsBoard
Connect the new rule with the ‘Root Rule Chain’:
  From the list of ‘Rule chain’ select the ‘Root Rule Chain’
  Create a diagram (image)
    Rule chain:
      write name (e.g. Create Telemetry Alarm)
      name of the new rule (e.g. Telemetry Rules)
    Arrow: select condition (e.g. True, False, Success, None)
  Save

## Slide 24: PYNQ-Z1 Setup
Set the JP4/Boot jumper to the SD position by placing the jumper over the top two pins of JP4 as shown in the image. (This sets the board to boot from the Micro-SD card).
To power the PYNQ-Z1 from the micro-USB cable, set the JP5/Power jumper to the USB position.
Getting Started: PYNQ Z1 Setup GitHub PYNQ Releases Downloadable PYNQ images

## Slide 25: PYNQ-Z1 Setup
Insert the MicroSD card loaded with the PYNQ-Z1 image into the Micro SD card slot underneath the board.
Connect the USB cable to your PC/Laptop, and to the PROG - UART/J14 MicroUSB port on the board.
Connect the board to Ethernet by following the instructions below
Turn on the PYNQ-Z1
Getting Started: PYNQ Z1 Setup GitHub PYNQ Releases Downloadable PYNQ images

## Slide 26: Network Connection
You will need to have an Ethernet port available on your computer, and you will need to have permissions to configure your network interface.
With a direct connection, you will be able to use PYNQ, but unless you can bridge the Ethernet connection to the board to an Internet connection on your computer, your board will not have Internet access.
You will be unable to update or load new packages without Internet access.
Assign a static IP address
Connect the board to your computer’s Ethernet port
Browse to http://192.168.2.99.
Password: xilinx

## Slide 27: Alternative Connections
Serial connection:
Use tools like PuTTY (link)
Port: COM_
Bauds/Speed: 115200
User: xilinx
Password: xilinx
Ssh connection:
User: xilinx
Password: xilinx
Example:
  ssh xilinx@192.168.2.99
In case of network problem:
Use serial connection
Execute:
  sudo /etc/init.d/networking restart

## Slide 28: Installation
For PYNQ boards, all commands below must be prefixed with sudo or by first going into sudo su. So:
  source /usr/local/share/pynq-venv/bin/activate
  python3 -m pip install --upgrade pip setuptools
  pip3 install tb-mqtt-client mmh3 pymmh3
Retrieve the example Jupyter notebooks using the PYNQ get-notebooks command.
  cd /home/xilinx/jupyter_notebooks
  pynq get-notebooks --from-package thingsboard -p . –force
You can now navigate the provided Jupyter notebook examples.

## Slide 29: Collect Telemetry Data
Collect Telemetry data and sent it to ThingsBoard:
  cpu_usage
  ip_address
  mac_ address
  processes_count
  swap_memory_usage
  ram_usage
  avg_load
  boot_time
  battery_level
import psutil def collect_telemetry_data(): return { "cpu_usage": psutil.cpu_percent(interval=1), …… "ram_usage": psutil.virtual_memory().percent}

## Slide 30: Connect PYNQ to ThingsBoard
MQTT Client
MQTT
Broker
ThingsBoard
Gateway

## Slide 31: Connect PYNQ to ThingsBoard
Obtain the access token:
  Once the device is created, it will appear in the devices list.
  Click on the device name to view its details.
  Navigate to the "Manage credentials" section.
  Copy the Access Token displayed. This token will be used for MQTT authentication.
Configuration of MQTT client:
  Broker Host: ThingsBoard server address (e.g., localhost)
  Port: 1883 (default MQTT port for non-SSL connections)
  Username: The access token of your device
  Password: Leave blank
Check connectivity

## Slide 32: Python Code Pubblish
import time from telemetry import collect_telemetry_data from tb_device_mqtt import TBDeviceMqttClient, TBPublishInfo THINGSBOARD_HOST = ‘192.168.2.X’ ACCESS_TOKEN = 'pg4iiosxgbkonzwpxpfb' def main(): client = TBDeviceMqttClient(
THINGSBOARD_HOST, username=ACCESS_TOKEN) client.connect() try: while True: telemetry_data = collect_telemetry_data()
print("Collected telemetry data:", telemetry_data)
result = client.send_telemetry(telemetry_data) success = result.get() == TBPublishInfo.TB_ERR_SUCCESS
if success: print("Telemetry data sent successfully.") else: print("Failed to send telemetry data.") time.sleep(10) except KeyboardInterrupt: print("Exiting...") finally: client.disconnect() if __name__ == "__main__": main()
Reference GitHub example

## Slide 33: Python Code Request
import time from tb_device_mqtt import TBDeviceMqttClient THINGSBOARD_HOST = ' 192.168.2.X ' ACCESS_TOKEN = 'pg4iiosxgbkonzwpxpfb' def on_attributes_change(client,result, exception): if exception is not None: print("Exception: " + str(exception)) else: print(result) def main(): client = TBDeviceMqttClient(
THINGSBOARD_HOST, username=ACCESS_TOKEN)
client.connect()
client.request_attributes(
["cpu_usage","ram_usage"], callback=on_attributes_change) try: while True: time.sleep(1) except KeyboardInterrupt: print("Exiting...") finally: client.disconnect()
if __name__ == "__main__": main()
Reference GitHub example

## Slide 34: Python Code Subscription
import time from tb_device_mqtt import TBDeviceMqttClient THINGSBOARD_HOST = ' 192.168.2.X ' ACCESS_TOKEN = 'pg4iiosxgbkonzwpxpfb' def on_attributes_change(client, result, exception): if exception is not None: print("Exception: " + str(exception)) else: print(result) def main(): client = TBDeviceMqttClient(
THINGSBOARD_HOST, username=ACCESS_TOKEN) client.connect()
client.subscribe_to_attribute(
"cpu_usage",
on_attributes_change)
client.subscribe_to_all_attributes(on_attributes_change) try: while True: time.sleep(1) except KeyboardInterrupt: print("Exiting...") finally: client.disconnect()
if __name__ == "__main__": main()
Reference GitHub example

## Slide 35: IoT & IoMT Sensors
Sensors
Healtcare:
  PYNQ-leds integration
  PYNQ-buttons integration
Ambiental:
  Light sensor Sparkfun TEMT 6000

## Slide 36: IoT & IoMT Sensors
Healtcare:
  PYNQ-leds integration: OK
  PYNQ-buttons integration: OK
  Heart rate and oximeter sensor MAX30102: I2C
Ambiental:
  Light sensor Sparkfun TEMT 6000: OK, KY-018 used
  Temperature and humidity sensor DHT11: GPIO
  Gas detector: Calibration?
    Gas and smoke detector MQ-2
    Carbon monoxide, methane, and LPG detector MQ-9
    Ammonia vapor and nitrogen oxides detector MQ-135

## Slide 37: Temperature and humidity sensor DHT11
Protocol: single-wire bi-directional
  Requirement: precise timing at the microsecond level
Problem:
  Slow (~2*10^3 ms to change r/w)
Solution:
  Implement RTL code for direct sensor communication.
  Consider using the Microblaze soft processor for handling timing-critical operations

## Slide 38: Heart rate and oximeter sensor MAX30102
Protocol: I2C
  Requirement: precise timing
Problem:
  Same of DHT11
Solution:
  Implement I2C protocol

## Slide 39: Gas sensor MQ-2, MQ-9, MQ-135
Protocol: -
  Read from analog pin
Problem:
  Calibration
Solution:
  Calibrate

## Slide 40: Sensors Code: Analog Reading
Sensors:
  Gas sensor: MQ-2, MQ-9, MQ-135
  Light sensor Sparkfun TEMT 6000

## Slide 41: Sensors Code: I/O
Sensors:
  Led
  Buttons
Assignment:
  Set alarm pressing buttons[0] (send to ThingBoard)
  Reset alarm pressing buttons[1] (send to ThingBoard)
  Turn On/Off leds[0] if alarm is set
from pynq.overlays.base import BaseOverlay base = BaseOverlay("base.bit") print("Press buttons to toggle corresponding LEDs") while True: for i, button in enumerate(base.buttons): if button.read(): base.leds[i].toggle()

## Slide 42: Summary
ThingsBoard:
  Setup
  Create:
    Device
    Asset
    Dashboards:
    Healtcare & Ambiental
    Telemetry
    Alarms
PYNQ:
  Setup
  Connect to ThingsBoard
  Connect sensor
Getting started: ThingsBoard
Getting Started: PYNQ Z1 Setup